## Slide 1
NEW TEAMMATE PROJECT BRIEF
Quadruped Robot
Project Onboarding
C++ whole-robot control, mechanical-dynamical architecture, and Stage 2 roadmap
Presentation date: Aug 29, 2026
Source snapshot: f3c5199
12 motors
4 legs x 3 joints
SocketCAN control
Notes: Open by framing this as an engineering onboarding session, not just a demo recap.
Use Aug 29, 2026 because the user said the presentation is tomorrow from the Aug 28, 2026 working date.
[Sources]
- README.md:3-8 states this is the C++ quadruped control repo and motor-control targets use Raspberry Pi/Linux SocketCAN.
- CMakeLists.txt:10-11,25,58,119,168-172 show C++23, low-level actuator, robot model, IMU reader, and quadruped_robot_locomotion_v3 target linkage.

## Slide 2
INTRODUCTION
What we are building
A physical quadruped platform where mechanical design, embedded sensing, CAN control, and locomotion software meet.
Mechanical body
CAD / URDF / MuJoCo model, four legs, custom actuator assemblies.
Whole-robot C++
Linux process centered on quadruped_robot_locomotion_v3.
Motor network
SocketCAN routes commands and feedback for twelve motor drivers.
Learning platform
Each teammate can own a sub-system and produce measurable evidence.
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Main talk track: this project is both a robot and a training ground. New teammates should see where their work can plug in.
Say explicitly that the deck is source-grounded where possible, but hardware status comes from the presenter's current report.
[Sources]
- README.md:3-8 identifies the C++ quadruped control programs and Raspberry Pi/Linux SocketCAN boundary.
- Simulation/mujoco/README.md:3-23 describes preparing a SolidWorks URDF as a MuJoCo-ready model.
- robot_hardware_config.h:15-24 lists four legs, four CAN channels, twelve motors, and 25:1 gear ratios.

## Slide 3
OBJECTIVE
Build a reliable quadruped learning platform
The engineering goal is controlled locomotion; the team goal is ownership, evidence, and practical robotics experience.
Project objective
Progress from deliberate walking to reliable dynamic locomotion while making every subsystem inspectable, testable, and teachable.
Locomotion
Stable gait states, foot targets, IK/FK, and validated hardware trials.
Hardware
Lower mass, better actuator behavior, cleaner wiring, and repeatable calibration.
Safety
Fresh feedback, loop timing checks, safe stop, and telemetry during every run.
Simulation
Use MuJoCo to de-risk gait changes before hardware testing.
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Explain the dual objective: make the robot walk better and make the project a place where teammates gain real skill.
Use the four objective lanes to invite teammates into a concrete sub-system.
[Sources]
- CMakeLists.txt:25-33,58-80,132-173 show the source split across low-level actuator, robot model, leg controllers, Xbox input, IMU reader, and the active executable.
- Simulation/mujoco/README.md:41-51 says simulation samples the current C++ trajectory/gait/FK/IK sources and drives all 12 joints in MuJoCo.

## Slide 4
CURRENT STATUS
Stage 1 proved movement; Stage 2 is reliability
Keep the source capabilities and hardware-verified behavior separate.
Stage 1: current demo baseline
- Hardware report: able to walk reversely
- Not yet reliable for lateral walking or yawing
- Source already contains lateral/yaw profile logic, so code capability is ahead of demonstrated behavior
- Baseline still needs repeatability evidence
Stage 2: next engineering target
- More dynamic walking
- More reliable locomotion
- Better actuators and a lighter robot
- Advance toward MIT mode and MPC after feedback and model quality improve
evidence gate
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Presenter status claim: Stage 1 reverse walking, not lateral/yawing yet, comes from the user's request in this session, not from a repo test log.
Important phrasing: the code has lateral and yaw paths, but that is not the same as hardware-verified lateral/yaw locomotion.
[Sources]
- User-provided status in Aug 28, 2026 request: Stage 1 reverse walking; not lateral or yawing; Stage 2 aims at dynamic and reliable locomotion.
- xbox_controller.h:41-46 and xbox_controller.cpp:254-267 show forward, lateral, yaw, vertical step input fields and the Right Bumper enable gate.
- robotGaitControl.cpp:253-349 and quadruped_trajectory.h:7-10 show profile selection for forward/cycloidal, lateral, yaw, and vertical step modes.

## Slide 5
MECHANICAL DYNAMICS
CAD model and physical architecture
Stage 2 needs a model that matches the real robot closely enough for control decisions.
Body + four legs
Each leg has hip, thigh, and shank joints, for 12 commanded joints total.
Actuator assemblies
Cycloidal actuator visuals exist in the MuJoCo prep path; real torque linkage modeling remains a caveat.
Mass properties
CAD/URDF/MJCF mass, COM, inertia, and collision geometry need numerical validation before model-based control.
Contact model
Ground contact and friction exist in simulation; hardware contact detection is not proved by this C++ source.
Stage 2 dynamics model target
M(q) qddot + C(q,qdot) qdot + g(q) = S^T tau + J_c(q)^T lambda
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Use this slide to explain why mechanical accuracy matters: model-based control is only as useful as the mass, inertia, actuator, and contact assumptions.
The dynamics equation is a Stage 2 control-model target, not evidence that the current C++ loop solves full-body dynamics.
[Sources]
- robot_hardware_config.h:15-24 gives four leg configs, twelve device IDs, four CAN channels, and 25:1 reductions.
- Simulation/mujoco/README.md:3-23 describes preparing the SolidWorks URDF as a MuJoCo-ready visual copy.
- Simulation/mujoco/README.md:146-163 describes COM markers, 11.84 kg model mass, 25:1 reduction, idealized joint-side gains, and provisional collision/friction/servo assumptions.
- Simulation/mujoco/README.md:165-192 says cycloidal actuator visuals do not change mass, COM, inertia, collision, or RL dynamics and physics-ready geometry must be added separately.
- Memory-derived older CAD report note: 17.18 kg and assembly-level mass/COM override concerns may be stale and should be rechecked before presenting as current CAD truth.

## Slide 6
RUNTIME COMMAND PATH
From joystick intent to twelve actuators
Centered on quadruped_robot_locomotion_v3
Human / operator
Xbox controller
/dev/input/js0
Xbox_Input
XboxController
readInputCommand()
Main loop
timing + state
v3 executable
Gait control
RobotGaitControl
profile + gait phase
Trajectory
quadruped_trajectory.cpp
foot targets
Robot
all-leg trajectory
command
Leg objects
4 leg values
IK/FK/Jacobian
Joint objects
12 joint values
fresh feedback + targets
CAN layer
MotorController
CanBusManager
Hardware
Linux SocketCAN
12 motor drivers
Boundary: Linux process
Boundary: SocketCAN network
Source snapshot f3c5199
Notes: Talk through this in one clear path: input command, gait state, foot trajectory, robot/leg/joint command generation, motor PDO command, SocketCAN, drivers.
Do not imply closed-loop balance or contact detection here. The feedback path is on the safety slide.
[Sources]
- quadruped_robot_locomotion_v3.cpp:30-36 creates RobotGaitControl, Robot, RobotShutdownGuard, and XboxController('/dev/input/js0').
- quadruped_robot_locomotion_v3.cpp:243-244 reads xbox::readInputCommand(controller).
- quadruped_robot_locomotion_v3.cpp:278-316 updates walking/landing and calls Robot::CalculateAllTrajectoryCommand().
- quadruped_robot_locomotion_v3.cpp:336-345 commands all legs by PDO and prints telemetry.
- joint.cpp:507-515 writes position and velocity by PDO2; can_bus_manager.cpp:53-85 routes received frames to MotorController::handleFrame.
- socketcan.cpp:70-88 opens PF_CAN/CAN_RAW; socketcan.cpp:112-122 and 165-187 write/read CAN frames.

## Slide 7
C++ OWNERSHIP
Robot owns Legs; Legs own Joints; Joints own Motors
This relationship is the cleanest mental model for new teammates reading the control code.
Robot
owns hardware_config_ and 4 Leg values
Leg
front_left
Leg
front_right
Leg
rear_left
Leg
rear_right
Inside each Leg
CanBusManager bus
Joint hip
Joint thigh
Joint shank
Inside each Joint
CanBusManager & bus
MotorController motor
name, gear ratio, direction
CAN routing
MotorController registers with CanBusManager;
receiveLoop dispatches frames by device id.
hardware config maps leg -> can channel -> device ids -> motor signs
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: This is the add-on schematic relationship the user asked for earlier, now as a slide.
Key explanation: Robot contains Leg values directly. Leg contains one bus and three Joint values. Joint owns its MotorController and keeps a reference to the Leg's bus.
[Sources]
- robot.h:199-204 and robot.cpp:9-23 show Robot's hardware_config_ and four owned Leg members returned by getLegs().
- leg.h:191-196 shows each Leg contains LegHardwareConfig, CanBusManager bus, Joint hip, Joint thigh, and Joint shank.
- joint.h:196-197 shows Joint stores CanBusManager& bus and MotorController motor; joint.cpp:37-45 constructs motor(&bus, device_id).
- can_bus_manager.h:41-47 and can_bus_manager.cpp:14-37,53-85 show motor registration and receiveLoop frame dispatch.
- robot_hardware_config.h:15-24 maps each leg to can1-can4, motor device IDs 1-12, 25:1 gear ratio, and direction signs.

## Slide 8
CURRENT GAIT PATH
Gait state drives foot targets, then joint targets
The current controller is kinematic trajectory tracking with safety checks, not full-body closed-loop balance.
InputCommand
RB enable gate
Motion profile
forward / lateral / yaw / vertical
Run state
Standing / Walking / Landing
Gait phase
master phase + leg offsets
Foot target
p_d and v_d
Joint target
IK + damped Jacobian
Current command math in the leg loop
p_d[k] = p_0 + r_profile(phi_k)
q_ik[k] = IK(p_d[k])
v_d[k] = (p_d[k] - p_d[k-1]) / dt
qdot_cmd = sat(J_lambda^{-1} v_d + K_p(q_ik - q), qdot_max)
q_next = q + dt qdot_cmd
What is not proved by this source
No inferred joystick signs
No source-proved closed-loop balance
No source-proved contact detection
No hardware-verified lateral/yaw claim
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: This slide is for explaining the live walking code at a systems level.
Say that forward/lateral/yaw/vertical profiles exist in code, but current hardware demonstration status is narrower.
[Sources]
- xbox_controller.h:41-46 and xbox_controller.cpp:254-267 define InputCommand fields and the Right Bumper enable gate.
- robotGaitControl.h:65-70 defines Standing, Walking, and Landing; robotGaitControl.cpp:364-447 performs walking/landing state updates.
- robotGaitControl.cpp:253-349 selects forward, lateral, turning, and vertical stepping profiles.
- quadruped_trajectory.cpp:181-190 dispatches CycloidalTrot, VerticalStep, LeftToRight, and CircularYaw foot trajectories.
- leg.cpp:462-519 uses analytical IK, the forward Jacobian, damped inverse Jacobian, velocity command limiting, and integrated next joint target.

## Slide 9
KINEMATICS
The math teammates should recognize
These formulas describe how foot motion becomes joint motion in the current control path.
Forward kinematics
p_foot = f(q)
q = [q_hip, q_thigh, q_shank]^T
Use this to estimate measured foot position.
Analytical inverse kinematics
q_ik = IK(p_d)
cos(theta) arguments are clamped before acos()
Use this to get desired joint position.
Jacobian velocity mapping
v_foot = J(q) qdot
J_lambda^{-1} = (J^T J + lambda^2 I)^{-1} J^T
qdot_des = J_lambda^{-1} v_d
Force to torque map for future MIT/force work
tau_joint = J(q)^T F_foot
tau_motor = tau_joint / gear_ratio
Simulation uses this in a torque-only experiment, not as the active hardware controller.
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Keep this concise: FK tells where the foot is, IK tells what joint angles reach a desired foot point, Jacobian maps velocity, and J^T maps force to torque.
The torque map belongs to future force/MIT-style control discussions; the active C++ command path sends position/velocity targets.
[Sources]
- leg.cpp:601-747 contains the FK, analytical IK, forward Jacobian, and damped inverse Jacobian implementations.
- leg.cpp:462-519 shows the current trajectory command uses IK and damped Jacobian-based velocity before command limiting.
- Simulation/mujoco/README.md:69-96 documents a torque-only Cartesian-force experiment using tau_joint = J.T @ foot_force and tau_motor = tau_joint / gear_ratio, and warns it is not a stable hardware controller.

## Slide 10
CONTROL ARCHITECTURE
Current method, plus PID, LQR, MPC, and MIT mode
Use this slide to orient teammates from today's code toward Stage 2 control.
Current C++ path
PDO2 position + velocity target
q_next = q + dt * qdot_cmd
Safety gates timing, freshness, tracking, velocity, homing
PID
e = r - y
u(t)=K_p e(t)+K_i int_0^t e(tau)dtau+K_d de/dt
LQR
x_{k+1}=A x_k + B u_k
u_k=-K x_k
K=(R+B^T P B)^{-1}B^T P A
MPC
min sum ||x_k-x_ref||_Q^2 + ||u_k||_R^2
s.t. dynamics, friction, torque, joint limits
MIT mode
tau = K_p(q_d-q)+K_d(qdot_d-qdot)+tau_ff
Needs validated actuator behavior and feedback freshness
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Make a clear distinction: PID/LQR/MPC/MIT formulas are teaching and roadmap material. The current C++ path is kinematic target generation plus PDO2 position/velocity commands.
For Stage 2, MIT mode and MPC are reasonable goals only after actuator behavior, model parameters, feedback timing, and safety boundaries are validated.
[Sources]
- joint.cpp:507-515 writes position/velocity target PDO2 frames.
- robot_safety.h:32-45 and robot_safety.cpp:8-88 define checks for control dt, feedback age, tracking, measured velocity, and homing motion.
- leg.cpp:462-519 shows the current kinematic command method.
- Memory-derived Recoil review note: PDO3 target plus feedforward torque resembled fixed-gain position impedance, not complete validated MIT control; recheck firmware before assigning Stage 2 work.

## Slide 11
SAFETY AND SENSING
Safety, telemetry, and partial IMU
This is the slide that prevents accidental overclaiming.
Joint feedback path
Motor position/velocity PDO feedback -> CanBusManager / MotorController -> Joint fresh-feedback checks -> Leg and Robot arrays -> RobotSafety -> main loop
Safety path
RobotSafety validates loop timing, feedback freshness, joint tracking, measured velocity, and homing. RobotShutdownGuard performs safe stop on exit.
Telemetry path
robot_telemetry.cpp receives control state, gait state, feedback, targets, timing, and speed scale. Keep it outside the command path.
IMU path
CMake links imu_uart_reader and Imu defaults to /dev/ttyAMA2, but quadruped_robot_locomotion_v3.cpp does not instantiate Imu. Current ESP32 source uses BNO055 + USB Serial, so label this in progress.
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Use this to explain how the robot avoids blind command streaming: timing, feedback, tracking, velocity, and homing checks are explicit.
IMU phrasing must be careful: reader library is linked, but not active in the main locomotion loop. The ESP32 source currently shows BNO055 and USB Serial, not a confirmed hardware-stabilizing UART link.
[Sources]
- motor_controller.cpp:490-543 stores PDO2 position/velocity feedback and exposes latest measurements.
- joint.cpp:505-642 reads fresh feedback and waits for fresh feedback.
- quadruped_robot_locomotion_v3.cpp:138-217 validates control dt and robot feedback before command generation.
- robot_safety.h:32-45 and robot_safety.cpp:8-88 define timing, feedback, tracking, velocity, and homing checks.
- robot.cpp:460-475 implements RobotShutdownGuard, whose destructor calls safeStopRobot unless dismissed.
- robot_telemetry.cpp:79-139 prints gait state, master phase, feedback, target position/velocity, timing, and speed scale.
- CMakeLists.txt:119-126 and 168-172 link imu_uart_reader; imu.h:29-37 describes the Pi UART reader and default /dev/ttyAMA2; quadruped_robot_locomotion_v3.cpp has no Imu instantiation.
- QUADRUPED-ESP32-IMU/src/main.cpp:10,174-183,239-263 show BNO055 setup and USB Serial output path; no Serial2/HardwareSerial packet sender was found in the inspected source.

## Slide 12
TEAM OWNERSHIP
What do you want to obtain from this project?
As leader, use their answers to assign subtasks that create real ownership and visible learning.
What skill do you want to gain?
Which subsystem do you want to own?
What deliverable would make you proud?
How much hardware risk do you want?
Mechanical / lightweight redesign
Actuator testing and MIT-mode bring-up
CAN reliability and safety instrumentation
Gait, IK/FK, MPC, and controls
MuJoCo simulation and validation
Docs, tests, telemetry, and onboarding
Source snapshot f3c5199
Notes: This slide is intentionally open-ended. It helps teammates tell you whether they want controls, mechanical design, firmware, simulation, safety, or documentation experience.
Suggested leader language: I want each person to own a small subsystem with a testable deliverable, so you can point to something real by the end of the stage.
[Sources]
- User explicitly requested an open-ended question so teammate tasks can be designed around ownership and experience.
- The ownership tracks come from the inspected code and repo structure: Control_Code/Locomotion, Xbox_Input, lowlevel_actuator, Simulation/mujoco, QUADRUPED-ESP32-IMU, and docs/archify.

## Slide 13
FUTURE PLAN
Stage 2 roadmap
Make the robot lighter, safer, and more dynamic. Advance only when evidence gates pass: source review, simulation, bench test, then hardware walking.
1. Baseline
Repeat reverse walking; log telemetry; define pass/fail criteria.
2. Hardware
Reduce mass/inertia; characterize actuators; validate gear ratios, signs, limits, and thermal behavior.
3. Low-level control
Bring up validated MIT-style torque/impedance mode with watchdogs and stale-target clearing.
4. Model control
Add state estimation, body dynamics, contact assumptions, and MPC preview planning.
5. Expand gaits
Reverse -> forward -> lateral -> yaw -> transitions -> disturbance tests.
Stage 2 decision rule
Do not upgrade the controller faster than the evidence: compile -> simulate -> bench -> tethered hardware -> untethered demo.
C++ repo snapshot f3c5199 | teammate onboarding | Aug 29, 2026
Notes: Close by assigning next steps around evidence. The roadmap is ambitious, but it should not skip validation.
If teammates ask why MPC cannot be first: it depends on model quality, actuator trust, contact assumptions, and state estimation.
[Sources]
- robot_safety.h:32-45 and robot_safety.cpp:8-88 show existing safety checks that Stage 2 should preserve and extend.
- Simulation/mujoco/README.md:41-51 and 69-96 show current simulation paths, including a source-sampled C++ trajectory runner and a torque experiment explicitly labeled not hardware-stable.
- Simulation/mujoco/README.md:146-163 and 189-192 describe provisional mass, COM, inertia, collision, and actuator modeling caveats.
- Memory-derived Recoil review note says MIT/PDO3-related firmware conclusions are unvalidated until source, build, flash, and hardware validation are repeated.